## Slide 1
Open-Source Dynamic Traffic Assignment Package
DTALite/NEXTA Classic Edition
(2017 September)
Xuesong Zhou
xzhou99@gmail.com
xzhou74@asu.edu

## Slide 2: Workshop Purpose and Objectives
Purpose
Educate workshop attendees on Dynamic Traffic Assignment modeling through hands-on exercises using the open-source DTALite software tool
Learning Objectives
Understand basic modeling approaches in DTALite
Import data to code and modify a subarea network
Evaluate simulation results using the visualization and reporting features in NeXTA
2
Notes: The purpose of the workshops is to educate attendees on Dynamic Traffic Assignment modeling using hands-on exercises with the open-source DTALite software tool. In general, the workshop will focus on understanding basic modeling approaches in DTALite, importing data in NeXTA, analyzing toll facilities and work zones, and evaluating simulation results using visualization and reporting features in NeXTA.

## Slide 3: Outline
Module 1: Introduction to DTALite/NeXTA
Module 2: Introduction to DTA modelling principles
Module 3: Visualization Features in NeXTA
Module 4: Introduction to Workshop Exercises
Module 5: Traffic Flow Theory
Module 6: OD Matrix Estimation
Module 7: Signalized Intersections Modeling
Module 8: VRP program
3
Notes: As I just mentioned, the webinar is divided into four parts, referring to four separate videos which make up this recorded session. This is the first session, where we’ll introduce you to DTALite and NeXTA, and provide an overview of our project development so far.

## Slide 4: Module 1 Introduction to DTALite/NeXTA
1.1 Project Objective and Motivations
1.2 What NeXTA/DTALite Can Do
1.3 Open-source Free Software Package

## Slide 5: Mesoscopic Traffic Simulation

## Slide 6: System Architecture and Data Flow

## Slide 7: Computational Efficiency

## Slide 8: 1.0 Traffic Flow Theoretical Foundation: LWR Equations
Hyperbolic system of conservation laws
  where q, k are flow and density, respectively, and g(·) is the net vehicle generation rate.
Traffic flow model
  Speed (or flow) of traffic is a function of density only
  E.g. Greenshields model: V = Vfree (1 – k/Kjam)

## Slide 9: Numerical Calculation Scheme Based on Link Flow/Density (Used in CTM)
Notation
  Δt = length of simulation interval (e.g. 1 sec, 6 sec)
  Δx = cell length (e.g. 0.5 mile)
  ki,t , vi,t =the prevailing density and mean speed in cell i during the tth time step
  qi,t = transfer flow rate from section i to cell i+1 during the tth time interval [t, t+Δt].
Computation Procedure
  Step 1: Calculate prevailing speed vi,t according to a traffic flow model
  Step 2: Calculate flow ready to move from cell i-1 to section i: vi,tki,t
  Step 3: Calculate transfer flow from section i to cell i+1
qi,t = Min { vi,t  ki,t , qmax i+1,t }
  Step 4: Update prevailing density at cell i
ki,t+1 = ki,t + (qi-1,t – qi,t)  Δt /Δ x
Issue: transfer flow qi,t is an explicit function of the occupancy at the current cell, other than the downstream capacity
    Transferred flow exceeds the spatial storage capacity at the next cell

## Slide 10: Newell’s N-Curve Approach (Used in DTALite)
Ni (t): cumulative flow counts at location i at time t
  q=[Ni(t+1)-Ni(t)]/Δt
  K=[Ni+1(t)-Ni(t)]/ΔX
Focus on N-curve at transfer points
  N=Min {Nupstream, Ndownstream}
Focus on change of N along a characteristic line (wave) at sections
  dN = (N/x)dx + (D/t)dt = - kdx + qdt =
  (-k+ q  wave)dx
  if wave=vfree, dN=( -k + k) dx=0
  if wave=w, dN=-(k+qw)dx= -kjamdx

## Slide 11: Illustration of N-Curve Computation For Tracking Queue Spillback

## Slide 12: Summary of Comparison
  CTM’s variables are density, incoming and outgoing flows and speed
  Newell’s variables are incoming and outgoing cumulative flow counts, from which the density and flows can be derived.
    We do not have direct speed measurements and link travel times are calculated from vehicle trajectories (with arrival times at upstream node and departure time at downstream node)

## Slide 13: Simulation Logic as Simple Queue
Can be viewed as pseudo event-based simulation and we do not simulate how a vehicle moves inside the link
Vehicle is moved into an in-flow queue at time ta
Calculate time entering the out-flow queue as ta+FFTT (free-flow travel time)
If the current simulation time t equals to or is later than ta+FFTT, if the link out capacity is still available, move this vehicle to the next link, otherwise stay in the out-flow queue
Out –flow
Queue
In-flow Queue
Available capacity
at every simulation interval
Notes: How to Determine Link-In Capacity at Each Simulation Interval
  Free-flow or partially congested  use pre-specified reduced capacity
  Fully congested according to N-Curve formula
    --> Link-out flow rate from the previous simulation interval
How to Determine Link-Out Capacity at Each Simulation Interval
Minimal of the following elements
  Pre-specified Average Capacity
  If a link is fully congested, its link-in capacity will be distributed to incoming links as function of lanes

## Slide 14: Network Traffic Flow Model
Goal: define boundary conditions for each link
  Downstream link capacity distribution at merges
  Outflow distribution at diverges
Congestion from downstream link:
  q(i1i)+q(i2 i)<= w  (kjam - ki,j(t))  Δ x
  or d1+d2<s
Outflow distribution: q(ii3)+q(i i4)=q(i)
  OD flow pattern, turning percentages

## Slide 15: In-Flow Capacity Distribution Schemes at Merges with two ramps or two freeways
Flows are assumed to be proportional to # of lanes
whenever supplies are not adequate,

## Slide 16: Traffic Flow Model at Diverge
As a meso-scopic model, DTALite moves vehicles with OD and path specific information instead of continuous flow
Outflow distribution is dependent on
  OD flow pattern, turning percentages

## Slide 17: Time-Dependent Shortest Path Algorithm
C++ implementation
    Use standard template library (STL) for complicating data structure (e.g. multi-dimensional vector, list, map (hash table)
    Customized efficient structure for shortest path algorithm
Multiple processor-oriented
      OpenMP technique for using multiple processors
Shortest path algorithm
  Label correcting with deque
  Single departure time, origin-based.
    The algorithm is called iteratively for each departure time to calculate shortest paths for all departure times

## Slide 18: What NeXTA/DTALite Can Do
Open-source traffic simulation/modeling Data Hub
    Integrated simulated and measured data management tools
    Connection with Travel demand model, signal optimization tool (Synchro)
Large-scale dynamic traffic assignment
    Typical network size: 2K~5K zones, 20K~50K links, 2~4 Million vehicles
Network scenario analysis
    Rich outputs: various operational performance measures
    Road pricing application: Consider time-dependent toll, Heterogeneous Value of times

## Slide 20: Connection with Traffic Sensor Data
  Import TMC GIS data directly to NEXTA
  Match TMC links with planning links using two layers
  Fetch speed data from Inrix layer to AMS data bub
  Compare the observed vs simulated results
Inrix Speed Data with TMC Codes
MPO Planning Data
Simulated vs Observed Path Travel Time

## Slide 21: 1.1 Project Objective and Motivations
Enhance DTALite to provide a rigorous and computationally efficient tool to evaluate road pricing and crash-reduction strategies
The enhanced tool will enable practitioners to:
Assess corridor and network-wide effects
Conduct numerous alternatives analyses
Evaluate recurring and non-recurring congestion
Calculate performance measures that can be applied in investment-level planning and decision making
21
Project Objective
Notes: The project objective was to enhance DTALite by providing a rigorous and computationally-efficient tool for evaluating road pricing and crash reduction strategies. The end goal was to enable practitioners to assess corridor and network-wide effects, leverage DTALite’s computational efficiency to conduct numerous alternatives analyses, evaluate recurring and non-recurring congestion, and calculate performance measures which can be applied in investment-level planning and decision making.

## Slide 22: Motivations
  Existing technical barriers (based on DTA user survey, TRB network modeling committee, 2009)
  - Require too many input data: 47%
  - Take too long to run: 35%
  - Model is unclear: 35%
  Our goals
  - Simplified data input from static traffic assignment
  - Use parallel computing capability, simplified routing and
  simulation
  - Open-source Visualization: Seeing is believing
  - Excel Tools: Start from basics
22
1.1 Project Objective and Motivations

## Slide 23: 1.2 What NeXTA/DTALite Can Do
Open-source traffic simulation/modeling Data Hub
    (1) Connection with signal optimization (Synchro) or microscopic simulation (VISSIM)
    (2) Integrated simulated and measured data management tools
Large-scale dynamic traffic assignment
    (1) Typical network size: 2000 zones, 20K links,1-2 Million vehicles
Network scenario analysis
    (1) Road pricing application: Consider time-dependent toll, Heterogeneous Value of times
    (2) Emission study: Fast simulation for emission analysis (with MOVES Lite)
    (3) Safety planning: Predict annual crash rates based on link type and traffic volume
23

## Slide 24: 1) Fast Simulation
  A rigorous and computationally efficient tool to evaluate numerous alternatives analyses
Network Statistics
Triangle Corridor Network (NC, USA)
Zones = 2,389
Nodes = 9,528
Links = 20,258
Signals = 1,914
AM Trips = 1,064,703
Households = 490,000
2 min. 45 sec. / iteration
1hour for 20 iterations
Computer System Specification:
  CPU: Intel i7-2960XM @ 2.70 GHz *8
  Memory: 16.0 GB
  System Type: 64-bit Windows 7
24
1.2 What NeXTA/DTALite Can Do

## Slide 25
Google Earth/Maps
Other Visualization
NeXTA
Large-scale Dynamic Traffic Assignment & Simulator
Corridor-level VOC contour
Simulation vs. Observation Comparison
25
2) Rich Output
1.2 What NeXTA/DTALite Can Do

## Slide 26
Field Data
Land Use, Safety & Emissions Models
HCM & Signal Timing Models
Micro-simulation Models
Dynamic Traffic Assignment Models
Travel Demand Forecasting Models
Data Hub
Field Data
Land Use, Safety & Emissions Models
HCM & Signal Timing Models
Micro-simulation Models
Dynamic Traffic Assignment Models
Travel Demand Forecasting Models
NeXTA Data Hub
Current Practice Ad Hoc
With NeXTA Data Hub Systematic
26
3) Integrated Modeling Practice
1.2 What NeXTA/DTALite Can Do

## Slide 27: 1.3 Open-source Free Software Package
NEXTA: front-end GUI (C++)
  Version 2: GUI for TRANSIMS and DYNASMART
  Version 3: GNU Open-source data hub
    Import
      Other regional planning models (TransCAD, VISSUM, Cube)
      GIS shape files (household data without node layer)
      Traffic volume, speed, GPS data, Google Public Transit Feed
    Export
      Google Earth, Google fusion tables
      Prepare network and signal data for
      Synchro and VISSIM (through QEM)
DTALite: Open-source computational engine (C++)
  Light-weight and agent-based DTA
  Built-in OD demand matrix estimation (ODME) program
27

## Slide 28: Useful Materials
DTALite Software Release
  https://github.com/xzhou99/dtalite_software_release
NeXTA/DTALite Training Materials
  https://github.com/xzhou99/learning-transportation/tree/master/lessons
DTALite Source Codes
  https://github.com/xzhou99/dtalite_beta_test
28

## Slide 29: Useful Materials
29
Installation required software packages
Datasets and Learning documents
User Guide

## Slide 30: Module 2 Introduction to DTA modelling principles
2.1 Dynamic Traffic Assignment Modelling Framework
2.2 Agent-based Routing
2.3 VOT Distribution
2.4 Multiple Traffic Simulation Models

## Slide 31: 2.1 DTA Modelling Framework
31
Notes: In general, the traffic simulation assigns vehicles to different paths based upon link travel time. The physical process of moving vehicles works in a two-step process. First, a vehicle is moved across a link during the link pass, and then moved between links at the node during the node pass. Link travel times from the traffic simulator are fed to the shortest path model for path selection. The new paths are then fed back into the traffic simulator in the next iteration.

## Slide 32
Common Assignment Methods
(1) Traffic Analysis Zone (TAZ)-based
  From zone centroid to zone centroid
  The same value of time for each type of vehicles
(2) Agent-based
  From activity location to activity location
  Each vehicle has its own value of time, value of information
  Important for road tolling analysis, traveler information provision study
32
2.2 Agent-based Routing

## Slide 33: 2.2 Agent-based Routing
Routing performed for each individual agent
Each agent has multiple dimensions of travel decisions
  Origin, destination, departure time, path
  Demand class (LOV, HOV, truck) or (HBW, HBO, NHB)
  Information class (Historical, Pre-trip, En-route)
33

## Slide 34
Individual generalized cost function
  Can consider multiple factors
    Value of time, Value of reliability, Value of safety
  Perform routing algorithm individually for each vehicle/agent
  Can adjust origin/destination/departure time/path at each iteration (day)
2.2 Agent-based Routing
34

## Slide 35: 2.3 VOT Distribution
Assumption:
  VOT : 50% of hourly rate (Concas and Kolpakov, 2009)
Best fit: Gen. Extreme Value (Orange)
Distribution will be used in DTALite: Lognormal (Blue).
Average VOT: 12 $/hour.
35

## Slide 36: 2.4 Multiple Traffic Simulation Models
BPR travel time functions
Point queue (relaxed storage constraints)
Spatial queue (similar to DYNASMART-P model)
Newell’s model (similar to Cell Transmission Model)
  Shockwave propagation
36

## Slide 37
Outflow capacity
Inflow capacity
Storage capacity
Exit Queue
Outflow Capacity
Inflow Capacity
Entrance List
Storage Capacity
37
Newell’s simplified kinematic wave model
2.4 Multiple Traffic Simulation Models

## Slide 38: 2.4 Multiple Traffic Simulation Models
  Triangular flow-density relationship
  Free flow speed, jam density, backward wave speed
Chart: Density (vpmpl)
| 0 | 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120 | 135 | 150 | 165 | 180
Flow | 0 | 900 | 1800 | 1620 | 1440 | 1260 | 1080 | 900 | 720 | 540 | 360 | 180 | 0
Chart: Density (vpmpl)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180
 | 60 | 60 | 60 | 60 | 60 | 60 | 60 | 49.7143 | 42 | 36 | 31.2 | 27.2727 | 24 | 21.2308 | 18.8571 | 16.8 | 15 | 13.4118 | 12 | 10.7368 | 9.6 | 8.5714 | 7.6364 | 6.7826 | 6 | 5.28 | 4.6154 | 4 | 3.4286 | 2.8966 | 2.4 | 1.9355 | 1.5 | 1.0909 | 0.70588 | 0.34286 | 0
38
Newell’s simplified kinematic wave model

## Slide 39: 2.4 Multiple Traffic Simulation Models
  Inflow capacity = outflow capacity
Outflow Capacity
Inflow Capacity
39
Queue propagation

## Slide 40: 2.4 Multiple Traffic Simulation Models
Node
Node Transfer
Check Outflow Capacity
Check Inflow Capacity
Check Storage Capacity
40
Node transfer
Notes: Going into more specifics, let’s take a closer look at the link pass and node pass. The capacity constraints are enforced at both ends of each link. At the beginning of the link, the entrance list keeps track of vehicles entering the link, enforcing the inflow capacity constraint. During the link pass, the vehicles are moved between the entrance list and the exit queue. The exit queue keeps track of vehicles waiting to leave the link, enforcing the outflow capacity constraint. Vehicles are then moved between the exit queue and the entrance list of the next link during the node.

## Slide 41
  Distribute inflow capacity to upstream links
  Lane & demand-based methods
Node
Available Inflow Capacity
80%
20%
41
2.4 Multiple Traffic Simulation Models
Merge Models

## Slide 42
  Different conditions by lane
  First-In-First-Out (FIFO) constraint
  Relaxation to prevent extreme bottlenecks
Node
42
2.4 Multiple Traffic Simulation Models
Diverge Models

## Slide 43
  Effective green time, saturation flow rate, movement-based capacity
  Relaxed inflow constraints
43
2.4 Multiple Traffic Simulation Models
Signalized Intersections

## Slide 44
  Input: Average hourly capacity, cycle time, offset at node
  Output: Effective green time per cycle(capacity/saturation flow rates)
44
2.4 Multiple Traffic Simulation Models
Signal Timing & Hourly Capacity

## Slide 45: Module 3 Visualization Features in NeXTA
3.1 Basic GUI features
3.2 View/Edit data files in NEXTA’s “project” menu
3.3 Integration with assignment model
3.4 Advanced visualization functions of NEXTA
3.5 MOE related display
3.6 Data exporting to Google Earth /GIS package

## Slide 46
3.1 Basic GUI features
Turn on and off GIS layers; Move around, select node and links; Toolbars for editing networks
Open project folder (CSV file format)

## Slide 47
3.1 Basic GUI features
Turn on and off GIS layers; Move around, select node and links; Toolbars for editing networks
Open project folder (CSV file format)

## Slide 48
3.2 View/Edit data files in “project” menu
Node/link/zone/activity location
Demand meta database
Scenario files

## Slide 49
3.3 Integration with assignment model
Traffic flow model
Traffic Assignment method

## Slide 50
3.4 Advanced visualization functions of NeXTA
24-hour Time control/Clock bar
Volume (bandwidth), density, speed
Animation and queue: (turn off node layer and bandwidth)

## Slide 51
3.4 Advanced visualization functions of NeXTA
24-hour Time control/Clock bar
Volume (bandwidth), density, speed
Animation and queue: (turn off node layer and bandwidth)

## Slide 52
3.5 MOE related display
Link-related display
Path-related display
Vehicle and Summary Charts

## Slide 53
3.5 MOE related display
Link-related display
Path-related display
Vehicle and Summary Charts

## Slide 54
3.5 MOE related display
Link-related display
Path-related display
Vehicle and Summary Charts

## Slide 55
3.5 MOE-related display
Link-related display
Path-related display
Vehicle and Summary Charts

## Slide 56
3.6 Export Data to Google Earth/GIS package
2D KML, 3D KML, GIS shape files
Google Earth visualization
Zone level display: adjust height/color

## Slide 57: Module 4 Introduction to Workshop Exercises
4.1 Data Preparation for Building A Regional Traffic Network
4.2 Clackamas Network Modeling(Calibration)

## Slide 58
58
4.1 Data Preparation for Building A Regional Traffic Network
Data Block | File Name
GIS Shape Files | 1a: node shape file
 | 1b: link shape file
 | 1c: zone shape file
GIS Importing Setting Files | 2: input_GIS_setting.csv
Advanced Definition Files | 3a: input_node_control_type.csv
 | 3b: input_link_type.csv
 | 3c: input_demand_type.csv
 | 3d: optional_vehicle_emission_rate.csv
Demand Files | 4.Demand files
Simulation Configuration Files | 5: input_demand_file_list.csv
 | 6. input_scenario_settings.csv
D: Scenario Files | 7a: sensor_count.csv
 | 7b: sensor_speed.csv
 | 8: Scenario_Work_Zone.csv
 | 9: Scenario_Dynamic_Message_Sign.csv
 | 10: Scenario_Link_Based_Toll.csv

## Slide 59: Step 1: Prepare Required Shape files
  node shape file (1a)
  link shape file (1b)
  zone shape file (1c) -- optional
  e.g. given shape files for the Atlanta network:
  - lod15AM_final_node.shp:
  provide node ID and coordinate values;
  - lod15AM_final_line.shp:
  provide from node id, to node id, length of links,
  link type, number of lanes of link, ect.
59
4.1 Data Preparation for Building A Regional Traffic Network

## Slide 60
60
Step 2: Extract GIS information from shape files –importing configuration
4.1 Data Preparation for Building A Regional Traffic Network
  The hub between shape files and NeXTA network data is import_GIS_settings.csv.(2)
  How to do the settings for import_GIS_settings.csv can be found at the learning document in “DTALite-NEXTA-Software-Package”
  [3] learning_document_GIS_importing.docx

## Slide 61
61
Step 3: Meta data files for building the network
4.1 Data Preparation for Building A Regional Traffic Network
  input_link_type.csv (3b)
  input_node_control_type.csv(3a) -- optional

## Slide 62
62
Step 4: Import GIS network to NeXTA
4.1 Data Preparation for Building A Regional Traffic Network
  Open NEXTA_GIS_Import.exe that is the only one program to generate traffic network;
  Click “File” ->“Import GIS Data Set”->“Next”. It will display the following dialogue.

## Slide 63
63
Step 4: Import GIS network to NeXTA
4.1 Data Preparation for Building A Regional Traffic Network
  Choose the import_GIS_setting.csv file and open it. It will display the right interface: those four csv files can be checked here.

## Slide 64
64
Step 4: Import GIS network to NeXTA
4.1 Data Preparation for Building A Regional Traffic Network
  Click “Import GIS Data” button. And the network will be generated.
GIS Shape files
NeXTA

## Slide 65
65
Step 5: Prepare Demand files
4.1 Data Preparation for Building A Regional Traffic Network
  Demand file (4) is the source of dynamic traffic assignment. Generally, it is provided by users. And all types of demand should be defined in Input_demand_type(3c)
  NeXTA can accommodate various demand formats:
  column format from VISUM,
  matrix format,
  full matrix format,
  Dynasmart format,
  agent file,
  and so on.

## Slide 66
66
Step 5: Prepare Demand files
4.1 Data Preparation for Building A Regional Traffic Network
  Input_demand_file_list.csv(5) is used to define the characteristics of demand data (4).

## Slide 67
67
Step 6: Data required for OD Demand calibration
4.1 Data Preparation for Building A Regional Traffic Network
  sensor_count.csv (7a)
  link_count , matched_link_from_node_id, matched_link_to_node_id;
  sensor_speed.csv(7b)
  speed_sensor_id , speed, population_count;
sensor_speed.csv
Sensor_count.csv

## Slide 68
68
Step 7: Work zone evaluation
4.1 Data Preparation for Building A Regional Traffic Network
  The setting file for work zone simulation is
  Scenario_Work_Zone.csv (8)
Scenario_Work_Zone.csv

## Slide 69
69
Step 8: VMS evaluation
4.1 Data Preparation for Building A Regional Traffic Network
  Scenario_Dynamic_Message_Sign.csv(9) is used to define the location and characteristics of variable message signs in the simulation
Scenario_Message_Sign.csv

## Slide 70
70
Step 9: Tolling evaluation
4.1 Data Preparation for Building A Regional Traffic Network
  Scenario_Link_Based_Toll.csv (10)
  Since the toll for different demand types is represented by money, the data Value of Time in input_demand_type.csv is important.
Scenario_Link_Based_Toll.csv

## Slide 71
71
Step 10: Emission evaluation(9a)
4.1 Data Preparation for Building A Regional Traffic Network
  optional_vehicle_emission_rate.csv (3d)
optional_vehicle_emission_rate.csv

## Slide 72
72
Step 11: Run Simulation
4.1 Data Preparation for Building A Regional Traffic Network
  Input_scenario_setting.csv (6)
Input_scenario_setting.csv

## Slide 73
Directly import important network attributes: Capacity, speed, number of lanes, etc.
First Simulation Run:
Wide-scale Gridlock (Red)
Converting from Macroscopioc Model to Mesoscopic Model
4.2 Clackamas Network Modeling(Calibration)
Notes: In our first example, let’s take a look at a simple macroscopic model that was converted for use with our mesoscopic model. We directly imported the network attributes, including capacity, speed, and the number of lanes. This creates an underlying assumption that the macroscopic capacities are compatible with the capacities in our mesoscopic model. In effect, we are using the macroscopic capacities for the capacity constraints in the DTA model. In our first simulation run, with very few adjustments, we found wide-scale gridlock, shown in red here. As you can see, they were appropriate in some locations in this model, mostly on freeways, but not so much in others. In this case, ramp capacities were causing significant queuing, and were creating more queuing in the arterial street network.

## Slide 74
Increased ramp outflow capacity
- Still experiencing significant queuing
Second Attempt
4.2 Clackamas Network Modeling(Calibration)

## Slide 75
Inflow/Storage Capacity?
4.2 Clackamas Network Modeling(Calibration)

## Slide 76
Two-lane ramp, coded with one lane
  - Reasonable outflow capacity
- Potential issues
  Underestimated inflow capacity
  - Underestimated storage capacity
Geometry Details
4.2 Clackamas Network Modeling(Calibration)
Notes: In this example, we find an interesting two-lane on-ramp entering the freeway. It begins as a two-lane facility, and enters the freeway as a one-lane facility. The ramp link was coded with one lane, which accurately represents the outflow capacity at the end of the link. However, since we’re missing a lane over a portion of the link, we’ve underestimated both the inflow capacity and storage capacity.

## Slide 77
Chart: Jam Density (veh/mile/lane)
| 120 | 140 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 240
Avg Travel Time (min) | 76.8595 | 49.0957 | 32.5099 | 17.3956 | 17.4283 | 12.0499 | 12.2612 | 11.1318 | 11.2126 | 10.6883
Avg Trip Time Index=(Mean TT/Free-flow TT) | 11.8373 | 7.2905 | 4.8453 | 2.5875 | 2.6548 | 1.9306 | 1.9648 | 1.8358 | 1.8325 | 1.7323
Avg Speed (mph) | 4.0175 | 6.1898 | 9.2239 | 17.1954 | 17.1209 | 24.403 | 23.7198 | 25.7562 | 25.4704 | 26.4556
Network Clearance Time (in min) | 1440 | 1440 | 1440 | 1364 | 1319 | 1316 | 1276 | 1244 | 1233 | 1214
Traffic Flow Model Sensitivity
4.2 Clackamas Network Modeling(Calibration)

## Slide 78
Reset outflow capacity, adjusted inflow & storage capacity
Third Attempt
4.2 Clackamas Network Modeling(Calibration)

## Slide 79
Combination of adjusting outflow and storage capacity appears more reasonable
4.2 Clackamas Network Modeling(Calibration)
Combined Modifications

## Slide 80
Macroscopic capacity may not be appropriate for mesoscopic capacity constraints
Understand the traffic flow model
  Understand limitations, special cases
Adjust capacity before OD demand, path flow
Start with fewer capacity constraints to remove possible unrealistic bottlenecks
  Point queue → Spatial queue → Shock wave → Speed-density relationships
4.2 Clackamas Network Modeling(Calibration)
Recommended Diagnostic Procedures

## Slide 81: Outline
Module 5: Traffic Flow Theory
Module 6: OD Matrix Estimation
Module 7: Signalized Intersections Modeling
Module 8: VRP code
81
Notes: As I just mentioned, the webinar is divided into four parts, referring to four separate videos which make up this recorded session. This is the first session, where we’ll introduce you to DTALite and NeXTA, and provide an overview of our project development so far.

## Slide 82
Synchronized display in NeXTA
82

## Slide 83: Vehicle Analysis Dialog

## Slide 84: Module 3: Modeling Approach
84

## Slide 85: Module 5 Traffic Flow Theory
5.1 Traffic Congestion Propagation: Understanding Theoretical Basics of Dynamic Traffic Network Assignment and Simulation
Contributing Author: Jiangtao Liu
https://scholar.google.com/citations?user=VLP4r4MAAAAJ&hl=en
5.2 Understand Network Equilibrium Model: Braess’ Paradox
Contributing Author: Tie Shi

## Slide 86: Learning Objectives
  (1) Understand major input and
  output data for a dynamic network
  loading program;
  (2) Identify bottlenecks and model congestion propagation;
  (3) Calculate traffic states through different computational approaches.
86
5.1 Traffic Congestion Propagation
  https://github.com/xzhou99/learning-transportation/tree/master/Lessons/Lesson%202/Data%20Set
Data Set

## Slide 87: Sample Case: 3-corridor Network
87
5.1 Traffic Congestion Propagation

## Slide 94
94
Graphical Method
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  U: interface between two different traffic states.
  State O: there is no traffic flow
  State A: the demand traffic enter the link 8->9
  State C: the steady traffic state of link 9->10
The flow-density relationship for different states of links

## Slide 96: Step 1: Check the value of traffic demand
  When Demand multiplier is 1.0, the hourly OD demand is 0.5*7200*1 = 3600 vehicles.
  The limit capacity of the path 1 is 3600, so now the demand is equal to the path capacity.
96
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  The traffic demand from origin zone 1 to destination zone 2 is 7200 vehicles in two hours. You can check value of traffic demand from “input_demand.csv” in the project folder.

## Slide 97
97
Step 2: Setup simulation settings
  Please use the following simulation settings shown in the flowing figure, and run simulation
  Link Traffic Flow Model: “Newell’s Kinematic Wave Model”
  # of Iterations/Days: 1
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)

## Slide 98
98
Step 3: View the result of simulation and analyze traffic states
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  View the simulation result: “Total Volume over Capacity Ratio” in the file output_summary.csv
from_node_id | to_node_id | type_code | link_type | link_length | start_time_in_min | end_time_in_min | total_link_volume | lane_capacity_in_vhc_per_hour | link_capacity_in_vhc_per_hour | volume_over_capacity_ratio
1 | 3 | f | Freeway | 1 | 420 | 540 | 7200 | 1900 | 5700 | 0.6316
3 | 4 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
4 | 5 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
5 | 6 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
6 | 7 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
7 | 8 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
8 | 9 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
10 | 11 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 3600 | 1
11 | 12 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 5400 | 0.6667
9 | 10 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 3600 | 1
12 | 2 | f | Freeway | 1 | 420 | 540 | 7200 | 1800 | 7200 | 0.5

## Slide 99
99
Step 3: View the traffic states of one path
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  Choose a path in the network
  Click on the “Density Contour”, “Speed Contour”, and “V/C Contour” to analyze the details of this traffic assignment.

## Slide 100
100
Step 3: View the traffic states of one path
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  Similarly, other analyses can also be displayed easily.
  link 9->10 and link 10->11 has a high density, which is consistent with the above “Total Volume over Capacity Ratio”.

## Slide 101
101
Step 4: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  Simulated lane volume of link 8->9

## Slide 102
102
Step 4: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  Simulated speed of link 8->9

## Slide 103
103
Step 4: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
  Simulated density of link 8->9

## Slide 104
104
Graphical Method
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
Vehicles’ trajectory in time-space diagram
  Speed
  The speed of link 8->9 and link 9->10 is the free flow speed, 60 mph, because the demand is equal to the capacity for the two links.

## Slide 105
105
Graphical Method
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
Vehicles’ trajectory in time-space diagram
  Density
  Link 8->9 is always at the state A and link 9->10 is at the state C, so its density is 60 vpmpl(link) for the both links.
  Meanwhile, about the density of each lane, link 8->9 is 20 vpmpl(lane) and link 9->10 is 30 vpmpl(lane).

## Slide 106
106
Graphical Method
5.1 Traffic Congestion Propagation
Case 1: demand = supply (multiplier = 1.0)
Vehicles’ trajectory in time-space diagram
  Propagation time: N/A

## Slide 107
107
Step 1: Check the value of traffic demand
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  When the demand multiplier is 1.2, the hourly OD demand is 0.5*7200*1.2 (4320).
  The limit capacity of the path 1 is 3600, so now the demand is slightly higher than the path capacity.
  As a result, a traffic congestion is formed and further propagated to the upstream corridor.

## Slide 108
108
Step 2: Setup simulation settings
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  Go to input_demad_file_list.csv
  Change the loading multiplier to 1.2 in the excel sheet
  Run the simulation for 1 iteration.

## Slide 109
109
Step 3: View link MOE of path 1
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  traffic congestion starts from link 8->9, and then propagates back to upstream links
  Then the traffic jam reaches the starting link 1->3 (without further space to accommodate the congestion), leading to continuously increasing density

## Slide 110
110
Step 4: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  Simulated speed of link 8->9

## Slide 111
111
Step 4: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  Simulated density of link 8->9

## Slide 112
112
Step 5: Describe traffic speed and density evolutions on links 7->8 and 8->9, Calculate the traffic congestion speed
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  The speed of link 8->9 changes from 60 mph to 15 mph in the first 20 min, and its density increases from 24 vpmpl to 80 vpmpl.
  To calculate traffic congestion propagation speed, we need to measure the propagation time and link length (1 mile)

## Slide 113
113
Step 5: Describe traffic speed and density evolutions on links 7->8 and 8->9, Calculate the traffic congestion speed
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  Select two links simultaneously, link 8->9 and link 7->8.
  Using key combination “ctrl +mouse click”, we can obtain the link MOE plot and then measure the queue propagation time.

## Slide 114
114
Step 5: Describe traffic speed and density evolutions on links 7->8 and 8->9, Calculate the traffic congestion speed
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  One can also precisely measure the exact propagation time duration using exported link MOE csv file.
  When the density (link 8->9) becomes 80, the corresponding time is 441min.
  When the density (link 7->8) becomes 80, the corresponding time is 455 min.
  Thus, the propagation time duration is 14 min.

## Slide 115
115
Graphical Method
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
  U: interface between two different traffic states.
  State O: there is no traffic flow
  State A: the demand traffic enter the link 8->9
  State B: the steady traffic state of link 8->9
  State C: the steady traffic state of link 9->10
The flow-density relationship for different states of links

## Slide 116
116
Graphical Method
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
Vehicles’ trajectory in time-space diagram
  Speed
  for link 8->9, at state A, its speed is 60 mph; at state B, due to the limitation of capacity, its speed is 15 mph.
  For link 9->10, the vehicles will drive at a speed based on the capacity, state C, whose speed is 60 mph;

## Slide 117
117
Graphical Method
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
Vehicles’ trajectory in time-space diagram
  Density
  for link 8->9, at the state A, its density is 72 vpmpl(link). After the propagation time, it is at the state B, whose density is 240 vpmpl(link).
  Meanwhile, the link 9->10 is always at the state C, whose density is 60 vpmpl(link).

## Slide 118
118
Graphical Method
5.1 Traffic Congestion Propagation
Case 2: demand > supply (multiplier = 1.2)
Vehicles’ trajectory in time-space diagram
  Propagation time: 14 min.

## Slide 119
119
Step 1: Check the value of traffic demand
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
  In this case, the demand OD is still 7200 from 7am to 9am,
  the multiplier is 1.3. so now the demand is much higher than the path capacity.
  The analysis process is the same as case 2 (0.5*7200*1.3 = 4680 vehicles).

## Slide 120
120
Step 2: Setup simulation settings
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
  Go to input_demad_file_list.csv
  Change the loading multiplier to 1.3 in the excel sheet
  Run the simulation for 1 iteration.

## Slide 121
121
Step 3: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
  Simulated speed of link 8->9

## Slide 122
122
Step 3: View link MOE of bottleneck links
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
  Simulated density of link 8->9

## Slide 123
123
Step 4: Describe traffic speed and density evolutions on links 7->8 and 8->9, Calculate the traffic congestion speed
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
  The speed of link 8->9 changes from 60 mph to 15 mph, and its density of one lane increases from 26 vpmpl to 80 vpmpl.
  A traffic congestion propagation time of 9 min can be observed in the following figure.

## Slide 124
124
Graphical Method
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
  U: interface between two different traffic states.
  State O: there is no traffic flow
  State A: the demand traffic enter the link 8->9
  State B: the steady traffic state of link 8->9
  State C: the steady traffic state of link 9->10
The flow-density relationship for different states of links

## Slide 125
125
Graphical Method
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
Vehicles’ trajectory in time-space diagram
  Speed
  For link 8->9, at state A, its speed is 60 mph; at state B, due to the limitation of capacity, its speed is 15 mph.
  For link 9->10, the vehicles will drive in a speed based on the capacity, state C, whose speed is 60 mph;

## Slide 126
126
Graphical Method
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
Vehicles’ trajectory in time-space diagram
  Density
  For link 8->9, at state A, its density is 78 vpmpl(link). After the propagation time, at state B, its density is 240 vpmpl.
  Meanwhile, the link 9->10 is always at the state C, whose density is 60 vpmpl(link). In addition, the method of calculating the density of each lane is the same as case 1.

## Slide 127
127
Graphical Method
5.1 Traffic Congestion Propagation
Case 3: demand > supply (multiplier = 1.3)
Vehicles’ trajectory in time-space diagram
  Propagation time: 9 min.

## Slide 128: 5.2 Traffic States as a result of demand-supply interactions
Base case without toll settings

## Slide 129
Input_demand_type
Scenario_Link_Based_Toll.csv

## Slide 130: Learning Objectives
  Understand modeling principles of user equilibrium
  Know how to setup BPR function parameters for special link types
  Understand the impact of adding a link and analyze the performance at link, path and network levels
  The impact of different levels of demand on Braess’ paradox
  Understand the impact of road pricing on Braess paradox and how to resolve Braess’ Paradox
130
5.2 Equilibrium Model: Braess’ Paradox
  http://en.wikipedia.org/wiki/Braess%27s_paradox
Source of Braess’ Paradox:

## Slide 131: Step 1: Locate a file called "NeXTA.exe " from the Braess Network Data Set and open the application.
131
5.2 Equilibrium Model: Braess’ Paradox
Task 1: Build a network for static traffic assignment, and configure BPR parameters

## Slide 132: Step 2: in NeXTA, open the Braess_Network.tnp from the Braess Network Data Set.
132
5.2 Equilibrium Model: Braess’ Paradox
Task 1: Build a network for static traffic assignment, and configure BPR parameters

## Slide 133: Step 2: in NeXTA, open the Braess_Network.tnp from the Braess Network Data Set.
133
5.2 Equilibrium Model: Braess’ Paradox
Task 1: Build a network for static traffic assignment, and configure BPR parameters

## Slide 134: Step 2: in NeXTA, open the Braess_Network.tnp from the Braess Network Data Set.
134
5.2 Equilibrium Model: Braess’ Paradox
Task 1: Build a network for static traffic assignment, and configure BPR parameters
  The following network file will be loaded into NeXTA, which has 4 nodes and 5 links.

## Slide 135: Step 2: in NeXTA, open the Braess_Network.tnp from the Braess Network Data Set.
135
5.2 Equilibrium Model: Braess’ Paradox
Task 1: Build a network for static traffic assignment, and configure BPR parameters
  For notational convenience, the following discussion denote link1->3; 4->2; 1->4; 3->2; 3->4 as a, b, c, d, e, respectively.

## Slide 136: Step 1: run simulation and view this data table by right-clicking and selecting 'View Link Data Table’ in link layer
136
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
 | Travel time function | Link Length | Lane capacity | # of lanes | BPR_alpha | BPR_beta
Links a, b | (v/100) | 0.01 | 1714 | 1 | 100 | 1
Links c, d | 45 min | 45 | 1900 | 3 | 0 | 1

## Slide 137: TT = FFTT[1 + ]
137
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  How do we specify the α and β for the links in Braess Network?
  t=T/100 is re-expressed as t=v/100 --> FFTT = 0.01; α = 100; c = 100; β=1. so that the reconstructed function is 0.01*(1+100v/100) = 0.01+ v/100, which is close to v/100.
Step 1: run simulation and view this data table by right-clicking and selecting 'View Link Data Table’ in link layer

## Slide 138: Step 2: Select a traffic flow model and Traffic Assignment Method.
138
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  Choose the option ‘Point Queue Model’ and 20 iterations.
  Run simulation

## Slide 139: Step 3: Review summary statistics
139
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment

## Slide 140: Step 4: Display the link volume.
140
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  First, click “config” (the button to the extreme left in NEXTA), which opens up a dialog box titled “Display Configuration”.

## Slide 141: Step 4: Display the link volume.
141
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  The volume values on each link are shown in the map as shown below.
link | a | b | c | d
Total Link Volume (vhc) | 2006 | 1994 | 1994 | 2006

## Slide 142: Step 5: Prepare statistics for the base case scenario.
142
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  Use the “vehicle” button to verify the path selection information

## Slide 143: Step 5: Prepare statistics for the base case scenario.
143
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  Select “1” under the tab “Origin Zone” and “2” under “Destination Zone”,

## Slide 144: Step 5: Prepare statistics for the base case scenario.
144
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  Click on the OD list populated, and then we can see the path list related to the demand, travel time at path 1.

## Slide 145: Step 6: Use the “summary” button to verify the overall network performance.
145
5.2 Equilibrium Model: Braess’ Paradox
Task 2: Run simulation for the Braess network to carry out traffic assignment
  Select the item “Avg Travel Time (min)” under the Y Axis drop-down list to show the average travel time in the network.

## Slide 146: Step 1: Click “Path” on the GIS Layer Panel Menu on the left side of your screen
146
5.2 Equilibrium Model: Braess’ Paradox
Task 3: Using NEXTA to display the shortest path in Braess network.
  Right click on Node 1 to choose the option “Direction from here”. Node 1 becomes a red highlighted box, ‘A’, indicating the start point of the shortest path

## Slide 147: Step 1: Click “Path” on the GIS Layer Panel Menu on the left side of your screen
147
5.2 Equilibrium Model: Braess’ Paradox
Task 3: Using NEXTA to display the shortest path in Braess network.
  Then right click on Node 2 to choose the option “Direction to here” and it becomes a red highlighted box, ‘B’.

## Slide 148: Step 2: Right click on node 4, click on the “avoid this node” menu
148
5.2 Equilibrium Model: Braess’ Paradox
Task 3: Using NEXTA to display the shortest path in Braess network.
  The shortest path from Node 1 to Node 2 is highlighted in the map as shown below.

## Slide 149: Step 2: Right click on node 4, click on the “avoid this node” menu
149
5.2 Equilibrium Model: Braess’ Paradox
Task 3: Using NEXTA to display the shortest path in Braess network.
  The path from node 1 to node 2 is now changed and no vehicle uses node 4 as it has been prevented.
 | Travel time | Flow
Path 1 | Link a(40.01) + Link d(45) = 85.01 min | 0
Path 2 | Link c(45) + Link b(40.01) = 85.01 min | 0
Path 3 | Link a(40.01)+ Link e(0.001)+ Link b(40.01) = 80.02 min | 4000

## Slide 150
150
5.2 Equilibrium Model: Braess’ Paradox
Task 4: Compare System-wide Performance Differences between Two Networks.
 | Without adding link e | Adding link e
Total number of vehicles | 4000 | 4000
System-wide total travel time | 260040.7 | 320083.8
Average travel time for each vehicles | 65.01 | 80.02
Volume on link a | 2006 | 4000
Volume on link c | 1994 | 0
Path 1 travel time | 65.07 | 85.01
Path 1 volume | 2006 | 0
Path 2 travel time | 64.95 | 85.01
Path 2 Volume | 1994 | 0
Path 3 travel time | —— | 80.02
Path 3 Volume | 0 | 4000
  The Braess paradox is a User Equilibrium (UE) system that is not necessarily System Optimal (SO).
  Under the UE principle, the users are assumed to be greedy and rational to choose their own route with minimum cost, and users are familiar with the system.

## Slide 151
151
5.2 Equilibrium Model: Braess’ Paradox
Task 4: Compare System-wide Performance Differences between Two Networks.
  Remarks:
  Comparing the average travel times before and after the addition of link e
  it is interesting that the average travel time increases from 65.01-min to 80.02-min, due to the addition of link e.
  After adding link e into the Braess Network, all the vehicles travel through link e, and the system-wide total travel time increases significantly.

## Slide 152
152
5.2 Equilibrium Model: Braess’ Paradox
Task 4: Compare System-wide Performance Differences between Two Networks.
  Remarks:
  However, for one single vehicle, the driver does not have an incentive to switch his route, as the travel times for the other two paths (Path 1 and Path 2) are 85.01 minutes when all the other vehicles travel through link e (except for that one vehicle).
  Therefore, there is a paradox on Braess network under reasonable assumptions, necessary and sufficient conditions in a general transportation network.
  It should be noted that the length of link e must be short enough to ensure that the travel time on path 3 is less than the travel times on both path 1 and 2.

## Slide 153: Step 1: Click “Toll” on the GIS Layer Panel, and then click to select link e.
153
5.2 Equilibrium Model: Braess’ Paradox
Task 5: Add a Link Toll and Run Static Simulation
  Set link e as a Toll link by clicking “Add Link-based Toll” in the right click drop-down list.

## Slide 154: Step 3: Run simulation on the new network and display the volumes on the map.
154
5.2 Equilibrium Model: Braess’ Paradox
Task 5: Add a Link Toll and Run Static Simulation
  We can see some vehicles shifting from Path 3 to Path 1 and Path 2 because of introducing the toll on path 3.
 | a | b | c | d | e
Total Link Volume(vhc) | 3837 | 3845 | 163 | 155 | 3682

## Slide 155: Step 1: Analysis of low demand on Braess Network
155
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  change the value of “Demand Loading Multiplier” at 0.1.
  Then, the demand will change into 4000*0.1=400 (the original demand is 4000 ).

## Slide 156: Step 1: Analysis of low demand on Braess Network
156
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  Run simulation using “BPR Function” as “Traffic Flow Model”
  “Method of Successive Average” as “Traffic Assignment Method” on Braess network
  display the volume value on the network.
 | a | b | c | d | e
Total Link Volume(vhc) | 400 | 400 | 0 | 0 | 400

## Slide 157: Step 1: Analysis of low demand on Braess Network
157
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  Keep the “Demand Loading Multiplier” at 0.1.
  Use BPR Function to run simulation and display the volume values on each link.
 | a | b | c | d | e
Total Link Volume(vhc) | 188 | 212 | 212 | 188 | 400

## Slide 158: Step 1: Analysis of low demand on Braess Network
158
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  Compare and analysis the system performance between two networks under low demand.
 | Without adding link e | Adding link e
System-wide travel time | 18806.88 | 3208.37
Volume on link a | 188 | 400
Volume on link c | 212 | 0
Path 1 travel time | 46.89 | 49.01
Path 1 volume | 188 | 0
Path 2 travel time | 47.13 | 49.01
Path 2 volume | 212 | 0
Path 3 travel time | —— | 8.02
Path 3 volume | 0 | 400

## Slide 159: Step 1: Analysis of low demand on Braess Network
159
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  From the statistics above, the system performance of the Braess network with link e is much better than the other’s.
  The travel time for a single vehicle or whole system decrease because of link e. Thus, no paradox occurs.

## Slide 160: Step 2: Analysis of high demand on Braess Network
160
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  change the value of “Demand Loading Multiplier” at 2.5.
  Then, the demand will change into 4000*2.5=10000 (the original demand is 4000 ).

## Slide 161: Step 2: Analysis of high demand on Braess Network
161
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  Choose “BPR Function” in “Traffic Flow Model” list
  “Method of Successive Average” in “Traffic Assignment Method” list on Braess network
  then click OK to start simulation. Display the volume values on the map.
 | a | b | c | d | e
Total Link Volume(vhc) | 5463 | 5020 | 4537 | 4980 | 483

## Slide 162: Step 2: Analysis of high demand on Braess Network
162
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  Keep “Demand Loading Multiplier” at 2.5
  Run the simulation using BPR Function to obtain the volume values on each link.
 | a | b | c | d
Total Link Volume(vhc) | 4827 | 5173 | 5173 | 4827

## Slide 163: Step 2: Analysis of high demand on Braess Network
163
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  Compare and analysis the system performance between two networks under high demand.
 | Without adding link e | Adding link e
System-wide travel time | 950698.6 | 978817.97
Volume on link a | 4827 | 5463
Volume on link c | 5173 | 4537
Path 1 travel time | 93.28 | 99.64
Path 1 volume | 4827 | 4980
Path 2 travel time | 96.74 | 95.21
Path 2 volume | 5173 | 4537
Path 3 travel time | —— | 104.85
Path 3 volume | 0 | 483

## Slide 164: Step 2: Analysis of high demand on Braess Network
164
5.2 Equilibrium Model: Braess’ Paradox
Task 6: Sensitivity analysis using different demand levels
  From the statistics above, not all vehicles take the path 3 because of link capacity limitation.
  And the travel time on path 3 is a little longer than other two paths’.
  Neither does paradox occur under high demand in Braess network.

## Slide 165: Module 6 Origin Demand Matrix Estimation
6.0 Background information

## Slide 166: Why is OD Demand Estimation Important?
Essential input for traffic assignment systems to support transportation network planning and operational decisions
Network
Traffic
Assignment
Performance
Measures
Capacity,
Traffic Control
OD
Demand
Notes: Formally, OD Demand can be definited as
Essential input …
In a traffic assignment system, we load OD demand into a traffic network with traffic control and information supply, provide a wide range of service measures in terms of as path flow, link flow and travel time
The Traffic assignment problem has been well studied in terms of formulation, solution algorithms mathematical properties.
How to obtain reliable OD demand input become the first priority for many most network planning and operational decisions, especially in calibration and validation
Even sophisticated traffic assignment procedure, inputing unreliable OD can still lead to problematic results
Garbage in and garbage out
Quality of OD demand info is critical for network planning and operational decisions, because how to provide sufficient supply in terms of transportation services to meet demand in terms of OD flows

## Slide 167: Why do We Need to Utilize Different Data Sources?
Advanced sensor technologies offer more reliable and less costly channels to provide real-time traffic flow measurements
Automatic Vehicle Identification
Loop Detector
Point Sensor
Point-to-point Sensor
Survey Data
Notes: Information overload?
Traditional survey methods cannot provide up-to-date dynamic demand inputs
  Model estimation based on social-economic and geographic data
  Survey samples from household, destination and roadside interviews
Advanced surveillance technologies offer more reliable and less costly channels to provide real-time traffic flow measurements
Common used loop detectors
My focus is ow
Turning Real-Time Data into Historical Data to
Support Strategic Decisions
Long term demand pattern
Time-consuming
Household, destination and roadside interview surveys, typically used in the transportation planning analysis, provide valuable samples about the detailed travel activities of each tripmaker, such as the origin and destination, the mode used and the travel time.
Populating OD demand patterns from survey samples, however, is a very costly and time-consuming process. Besides, the above traditional survey methods cannot provide up-to-date dynamic demand inputs required by on-line ATMS and ATIS applications.
more reliable and less costly channels to
Dynamic OD demand estimation can be viewed as a inverse problem of DTA
Data are overloaded

## Slide 168: How has OD Matrix Estimation been Done?
Upper level:
Constrained ordinary least-squares problem
Lower level:
  Link flow proportion = Traffic assignment ( )
OD Demand
Traffic Assignment
Flow Pattern
ODME Optimization Model
Link Proportions
Notes: Note: In dynamic context and especially in congested networks, link-flow proportions are not constant and are, themselves, a nonlinear function of the (unknown) OD demand values.

## Slide 169: What is Link-Flow Proportion?
Link Proportions (Assignment matrix)
Fraction of vehicular demand flow from OD pair( i, j) contributing to the flow on link l
OD pair 1->3 1->4 2->3 2->4
Link a 1 1 0 0
Link b 1 1 1 0.3
Link c 0 0 0 0.7
Path Flow Structure
Notes: OD Demand split for a network with all counts on entry exit links
Genea
The Link Proportion Matrix captures the effects of route
choice, travel time dispersion and departure
time
#“It is a complete description of the TEMPORAL-SPATIAL
characteristics of traffic on a Network”
Link flow proportions
mlj
od (assignment matrix) is
the fraction of OD flows dod[t]
observed on link l at
observation time j and
leaving their origins at [t] (i.e.
at or before time slice j)
od (assignment matrix) is
the fraction of OD flows dod[t]
observed on link l at
observation time j and
leaving their origins at [t] (i.

## Slide 170: Two Common Questions…
Travel time IS NOT the only factor in travel route choice utility function.
  A long list of additional route choice factors: Highway bias, distance consideration, # of signals, inherence preferences
    Do we need to reach the “perfect” travel-time-based UE in ODME?
2. Can we combine/integrate traffic assignment and OD demand estimation? (Both aim to adjust flows in a network)

## Slide 171: What is the Difficulty of Dynamic ODME under Congested Conditions?
  Single value of flow volume observation could correspond to free-flow and congested states
  No linear link proportions available for density and travel time measurements
Chart: Density (vhc/ml/lane)
Free
flow
Congested

## Slide 172: Our Proposed Approaches
1. Path Flow Adjustment
    Combine OD estimation/adjustment with traffic assignment
    Final solution is a set of path flow patterns satisfying “tolled user equilibrium”
2. Approximate Gradient Method
  Use spatial queue model to calculate link flow/density change due to incoming path flow change

## Slide 173: Objective Function: Minimize
Deviation between measured and estimated traffic states
Deviation between aggregated path flows and target OD flows
Demand flow target demand path flow target demand
(3) Gap Function to Quantify User Equilibrium Conditions

## Slide 174: Flow Chart of Algorithm
Path flow adjustment based on all gradients

## Slide 175: Example 1
Path | FFTT (min) | Capacity (veh/hr) | Assigned Flow (veh/hr) | Travel Time (min)
Path 1 | 20 | 3000 | 5400 | 56
Path 2 | 30 | 3000 | 2600 | 56
Congested two-link Corridor:
Total demand = 8000 veh/hour

## Slide 176: Path Flow Volume Convergence Pattern
Chart: Iteration
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Ground-truth total demand | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000 | 8000
Estimated total demand | 6000 | 7494.5 | 7868.8465 | 7963.3456 | 7987.7459 | 7994.449 | 7996.5817 | 7997.4579 | 7997.9339 | 7998.2451 | 7998.4667 | 7998.6296 | 7998.7508 | 7998.8412 | 7998.9088 | 7998.9593 | 7998.9971 | 7999.0253 | 7999.0465 | 7999.0623
Ground-truth flow on route 1 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400 | 5400
Estimated Flow on route 1 | 3000 | 4099.75 | 4550.8459 | 4795.5435 | 4955.4216 | 5069.2168 | 5152.8779 | 5215.0836 | 5261.5136 | 5296.2133 | 5322.1573 | 5341.5578 | 5356.0658 | 5366.9153 | 5375.029 | 5381.0966 | 5385.6342 | 5389.0276 | 5391.5653 | 5393.463
Estimated Flow on route 2 | 3000 | 3394.75 | 3318.0006 | 3167.8021 | 3032.3243 | 2925.2323 | 2843.7038 | 2782.3743 | 2736.4203 | 2702.0318 | 2676.3094 | 2657.0718 | 2642.6849 | 2631.9259 | 2623.8798 | 2617.8627 | 2613.3629 | 2609.9978 | 2607.4812 | 2605.5992
Ground-truth flow on route 1 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600 | 2600

## Slide 177: Path Travel Time Convergence Pattern
Chart: Iteration
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Estimated travel time on route 1 | 40 | 47.3317 | 50.339 | 51.9703 | 53.0361 | 53.7948 | 54.3525 | 54.7672 | 55.0768 | 55.3081 | 55.481 | 55.6104 | 55.7071 | 55.7794 | 55.8335 | 55.874 | 55.9042 | 55.9269 | 55.9438 | 55.9564
Estimated travel time on route 2 | 60 | 63.9475 | 63.18 | 61.678 | 60.3232 | 59.2523 | 58.437 | 57.8237 | 57.3642 | 57.0203 | 56.7631 | 56.5707 | 56.4268 | 56.3193 | 56.2388 | 56.1786 | 56.1336 | 56.1 | 56.0748 | 56.056
User equilibrium travel time | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56

## Slide 178: Algorithm Performance under Different Input Conditions
Information Availability |  |  |  | Estimation Result |  |  | 
Volume observations on path 1 only | Volume observations on path 2 only | Error-free target demand,8000vhc/hr | Error-free travel time on path 1 | Flow on path 1 | Flow on path 2 | Total estimated demand | Equilibrium travel time (min)
X |  |  |  | 5051.7 | 2367.8 | 7419.5 | 53.7
 | X |  |  | 4967.7 | 2311.8 | 7279.4 | 53.1
X | X |  |  | 5011.8 | 2341.2 | 7353.0 | 53.4
X | X | X |  | 5387.9 | 2592.0 | 7979.9 | 55.9
X | X | X | X | 5401.1 | 2600.7 | 8001.8 | 56.0

## Slide 179: Multi-objective Programming Perspective
Gap Function: Degree of deviation from the original user equilibrium solutions
Vary penalty on path cost to generate non-dominated solutions
Gap Function
Measurement deviation

## Slide 180: Sensitivity-Analysis and Gradient Information
Approximate the derivatives through simulation for each OD pair and each time interval in every iteration (Tavana, 2001)
Gradient approximation methods
  Simultaneous Perturbation Stochastic Approximation (SPSA) framework by Balakrishna et al. (2008); Cipriani et al. (2011)

## Slide 181: How to Use Spatial Queue Model to Evaluate Partial Derivatives with respect to Path Flow Perturbation? Case 1: Free-flow Conditions
Link inflow and outflow increase by 1 at entering time and leaving time, respectively.

## Slide 182: Case 2: Congested Condition
Inspired by study by Ghali and Smith (1995)

## Slide 183: Case 3: Two Partially Congested Links
The perturbation flow on the second link starts at the end of queue duration of the first link; rather than the vehicle entering time on second link
Here!
Not Here!
Similar work by Shen, Nie and Zhang (2007) for path marginal cost analysis

## Slide 184: Case 4: Queue Spillback
Individual extra delay depends on when the vehicle/perturbation flow joins in the queue.

## Slide 185: Summary
Integrated path-based OD demand estimation formulation
Gradient-based path flow adjustment process
Derive theoretically sound partial derivatives of link flow, density and travel time with respect to path flow perturbations

## Slide 186: Mathematical Details: Gradient Based Formulation
Individual gradients with respect to path flow adjustment
Adjust path flow on each path based on generalized gradient/Cost
Calculated based on the spatial queue model

## Slide 187: The process of one simulation for scenario analysis using estimated OD demand
187
6.1 OD Matrix Estimation Scenario
  For performing scenario analysis, such as work zone, incident, ramp metering, etc., the travel demand should be calibrated in advance.
  In this section, the integration of the two parts above is realized in DTALite through just one simulation, the process of which can be illustrated in the following Figure

## Slide 188: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_link.csv file
188
6.1 OD Matrix Estimation Scenario
  Set count sensor ID to “origin node -> destination node”
  Set speed sensor ID to “origin node -> destination node”

## Slide 189: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_scenario_setting.csv file
  so at least 30 iterations are required for the path flow adjustment for ODME
  Specify traffic assignment method to “3>ODME”
189
6.1 OD Matrix Estimation Scenario

## Slide 190: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_scenario_setting.csv file
  Specify start and end iteration of ODME (the iteration number indicate that ODME will begin at the 21th iteration and end at the 50th iteration)
190
6.1 OD Matrix Estimation Scenario

## Slide 191: Step 2: Prepare Specific Input File for Signal Scenario
  Sensor_count.csv file
  Specify count sensor ID, origin node ID and destination node ID of observed links
  Specify observation time period of observed links
191
6.1 OD Matrix Estimation Scenario

## Slide 192: Step 2: Prepare Specific Input File for Signal Scenario
  Sensor_speed.csv file
  Specify count sensor ID, origin node ID and destination node ID of observed links
  Specify observation speed of observed links
192
6.1 OD Matrix Estimation Scenario

## Slide 193
193
Step 3: Run Simulation and Perform Analysis
  checking output_summary.csv file, users can better understand the process of ODME in DTALite.
6.1 OD Matrix Estimation Scenario

## Slide 194
194
Step 3: Run Simulation and Perform Analysis
  For the first 20 iterations, a standard dynamic user equilibrium method, MAS, is used.
  It is expected to see the UE gap (Avg User Equilibirum (UE) gap (min) and Relative UE gap (%)) dramatically decreases and finally reach a stable state,
6.1 OD Matrix Estimation Scenario

## Slide 195
195
Step 3: Run Simulation and Perform Analysis
  Comparison result between observed link count and simulated link count after ODME
6.1 OD Matrix Estimation Scenario

## Slide 196: Module 7 Signalized Intersections Modeling
7.1 Link Based Signal Representation Model
7.2 Phase Based Signal Representation Model
7.3 Importing data from Synchro to DTALite
7.4. QEM (Signal Quick Estimation Method) Application to Generate signal timing data

## Slide 197: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_node.csv
  Set the control type of signal intersections to signalized type
  (e.g., the control type of node 5 is set to “pretimed signal” in this case)
197
7.1 Link Based Signal Representation Model

## Slide 198: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_link.csv
  Specify the number of left-turn lanes (including separated left-turn lanes and shared left-turn lanes)
198
7.1 Link Based Signal Representation Model

## Slide 199: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_scenario_setting.csv
  Set traffic flow model to “2> Spatial Queue Model”
  Set signal representation model to “1> link based signal
199
7.1 Link Based Signal Representation Model

## Slide 200: Step 2: Prepare Specific Input File for Signal Scenario
  Input_movement.csv
  Specify left-turn type movements and through-type movements which are required
200
7.1 Link Based Signal Representation Model

## Slide 201: Step 2: Prepare Specific Input File for Signal Scenario
  Input_signal.csv
  the number of phase plan
  starting time(in seconds), ending time(in seconds), cycle length(in seconds) and offset (in seconds) of each signal plan
201
7.1 Link Based Signal Representation Model

## Slide 202: Step 2: Prepare Specific Input File for Signal Scenario
  Input_signal.csv
  saturation flow(per hour per lane), start time(in seconds) and end time(in seconds) for through-type movement and left-turned movement
202
7.1 Link Based Signal Representation Model
Step 3: Run Simulation

## Slide 203: Step 1: Build a Basic Network and Prepare Necessary Input Files for Basic Scenario
  Input_node.csv
  Input_link.csv
  Setup data in these two files the same as “7.1 Link Based Signal Representation Model”
203
7.2 Phase Based Signal Representation Model

## Slide 204: Step 2: Parameter settings in key simulation configuration files
  Input_movement.csv
  Movement id
  turn direction
204
7.2 Phase Based Signal Representation Model

## Slide 205: Step 2: Parameter settings in key simulation configuration files
  input_signal_timing_plan.csv
  Intersection id
  Timing plan number
  Start time and end time of timing plan
  Starting phase
  Offset
205
7.2 Phase Based Signal Representation Model
[TOD] | int_id | timing_plan_no | from_time | to_time | starting_phase | off_set
 | 5 | 1 | 0 | 86400 | 1 | 11

## Slide 206: Step 2: Parameter settings in key simulation configuration files
  input_timing.csv
  Intersection id
  Timing plan number
  Number of phase
  green duration, movement string and movement direction string of phase
206
7.2 Phase Based Signal Representation Model
[Signal] | int_id | timing_plan_no | phase_id | next_phase | green_duration | movement_str | movement_dir_str
 | 5 | 1 | 1 | 2 | 120 | 1_3_T; 1_2_L; 3_1_T; 3_4_L | WBT; WBL; EBT; EBL;
 | 5 | 1 | 2 | 1 | 70 | 2_4_T; 2_3_L; 4_2_T; 4_1_L | SBT; SBL; NBT; NBL;

## Slide 207: Step 3: generate the input_timing_status.csv file with timing_generator.exe (Contributed by Prof. Pengfei Taylor Li, Currently maintained by the University of Maryland Prof. Lei Zhang’s Group )
  Required files include input_timing.csv file and input_signal_timing_plan.csv file
207
7.2 Phase Based Signal Representation Model
movement_str | start_time_in_sec | end_time_in_sec | signal_status | from_node_id | to_node_id | turn_type
1_3_T | 0 | 119 | 1 | 1 | 5 | T
1_2_L | 0 | 119 | 1 | 1 | 5 | L
3_1_T | 0 | 119 | 1 | 3 | 5 | T
3_4_L | 0 | 119 | 1 | 3 | 5 | L
2_4_T | 120 | 189 | 1 | 2 | 5 | T
2_3_L | 120 | 189 | 1 | 2 | 5 | L
4_2_T | 120 | 189 | 1 | 4 | 5 | T
4_1_L | 120 | 189 | 1 | 4 | 5 | L
… | … | … | … | … | … | …

## Slide 208
208
Step 3: NEXTA GUI instruction
  Load the example project
  Choose the Movement layer -> right click the intersection node -> View Movement Properties for Selected Node.
7.2 Phase Based Signal Representation Model

## Slide 209
209
Step 3: NEXTA GUI instruction
  If this section has the phase plan before, thus we could display them in NEXTA.
7.2 Phase Based Signal Representation Model

## Slide 210
210
Step 4: Add/delete a phase in current phase
  Add/delete a phase in current phase:
  Check the box before Movement-Phasing Edit Mode
  Double click the phase that you want to add/delete
7.2 Phase Based Signal Representation Model

## Slide 211
211
Step 4: Add/delete a phase in current phase
  then the corresponding movement_str will be changed in the table below
  Click save timing file button, the input_timing file will be updated in the folder.
7.2 Phase Based Signal Representation Model

## Slide 212
212
  Input_scenario_setting.csv
  Set traffic flow model to “2> Spatial Queue Model”
  Set signal representation model to “2> phase based signal”
7.2 Phase Based Signal Representation Model
Step 5: Run Simulation and Perform Analysis

## Slide 213
213
Step 1: Prepare the Synchro dataset
Export to LANES.cvs, LAYOUT.csv, PHASING.csv and TIMING.CSV (UTDF format).
7.3 Importing data from synchro to DTALite

## Slide 214
214
Step 1: Prepare the Synchro dataset
Export to LANES.cvs, LAYOUT.csv, PHASING.csv and TIMING.CSV (UTDF format).
7.3 Importing data from synchro to DTALite

## Slide 215
215
Step 2: Use nexta to import the synchro UTDF format.
  Open NEXTA, click tools -> Import Synchro UTDF File:
7.3 Importing data from synchro to DTALite

## Slide 216
216
Step 2: Use nexta to import the synchro UTDF format.
  Open LAYOUT.csv File
7.3 Importing data from synchro to DTALite

## Slide 217
217
Step 2: Use nexta to import the synchro UTDF format.
  The synchro data will be imported to NEXTA.
7.3 Importing data from synchro to DTALite

## Slide 218
218
Step 2: Use nexta to import the synchro UTDF format.
  Save the project in the same folder
7.3 Importing data from synchro to DTALite

## Slide 219
219
Step 2: Use nexta to import the synchro UTDF format.
  The network and the signal data will be automatically saved into the folder.
7.3 Importing data from synchro to DTALite

## Slide 220
220
Step 3: Mapping two networks
  In this step, we have two networks (a) DTALite main network (b) the imported synchro network in DTALite format.
  Rename the input_node.csv and input_link.csv to input_node_2.csv and input_link_2.csv and copy to our old DTALite network.
7.3 Importing data from synchro to DTALite

## Slide 221
221
Step 3: Mapping two networks
  Then, open the new project in NEXTA.
7.3 Importing data from synchro to DTALite

## Slide 222
222
Step 3: Mapping two networks
  Use lock/unlock reference network tool in reference line layer
7.3 Importing data from synchro to DTALite

## Slide 223
223
Step 3: Mapping two networks
  Move, zoom in and zoom out imported synchro network
7.3 Importing data from synchro to DTALite

## Slide 224
224
Step 3: Mapping two networks
  But now the node and Link ID of the two networks are different, we need to map them with our old DTALite Network.
  Based on this, we could have the input_node_mapping.csv table generated by ourselves manually.
  (e.g., Node_id_1 is the node id from the old DTALite network, node_id_2 is the mapping node from synchro exported network.)
7.3 Importing data from synchro to DTALite
node_id_1 | node_id_2
3346 | 251
3335 | 1208
3338 | 1505
… | …

## Slide 225
225
Step 3: Mapping two networks
  Get input_node_mapping.csv file in the last step
  Copy the input_timing_2.csv from the Synchro to the new folder.
  Then we could run the simulation of timing_movement_generater.exe and get the result of input_timing_mapping.csv:
7.3 Importing data from synchro to DTALite

## Slide 226
226
Step 3: Mapping two networks
  Verify the input phasing results and add required next phase number. in main DTA network
  Make sure the imported phasing data are correctly display in NEXTA.
7.3 Importing data from synchro to DTALite

## Slide 227: Generate default NEMA phasing for a signalized intersection
If a node is designated as a pretimed signal, and there is no input timing information provided, then NeXTA can generate the default NEMA phasing

## Slide 230
Movement & Phase Numbering
HCM 2010
Through Φ: even numbers (2,4,6,8)
Left turn Φ: odd numbers (1,3,5,7)
3-legged intersection LT can be even #
Φ 2 & 6 denote major street
Right turn Φ concurrent w/ through in most cases (no special RT Φ)
Contributing Author:
Dr. Milan Zlatkovic

## Slide 231
Ring-barrier diagram – graphical representation of phases within sets of rings & barriers (NEMA standard, all traffic controllers)
Ring – phases that operate in sequence (cannot time simultaneously)
Barrier - separation of intersecting movements to prevent operating conflicting phases at same time
Ring-Barrier Phase Structure
Split summations:
Φ 1+2+3+4 = C
Φ 5+6+7+8 = C
Exceptions?
Φ 1+2 = Φ 5+6
Φ 3+4 = Φ 7+8
Contributing Author:
Dr. Milan Zlatkovic

## Slide 232: 7.4 QEM (Signal Quick Estimation Method) Application
Contributing Author:
Dr. Milan Zlatkovic
Assistant Professor, University of Wyoming
http://www.uwyo.edu/civil/faculty_staff/faculty/milan-zlatkovic/index.html
Reference:
Integration of signal timing estimation model and dynamic traffic assignment in feedback loops: system design and case study
Milan Zlatkovic, Xuesong Zhou
Journal of Advanced Transportation 49 (6), 683-699, 2015

## Slide 234: QEM Application: Overview
  Challenges for Planners:
    How to obtain signal data? Especially for future year with dramatically changed traffic pattern??
    How do we obtain movement-specific capacity under prevailing traffic condition (e.g. different turning percentage) for a large number (100-500) of intersections?
  The QEM_SIG Excel spreadsheet that accompanies NeXTA represents a computational engine for estimating signalized intersections operation
  It relies on HCM 2010 and additional methodologies for computing parameters of signalized intersections
  Can be used as a stand-alone application, or integrated with NeXTA
  It is an open-source Excel application with friendly GUI for data input and viewing results

## Slide 235: QEM Application: Sections
  Sheet 1 – input/output sheet for communication with NeXTA
  Input sheet – data input section; this is the only section where the user needs to input intersection data
  Phase designation – assigns phases to intersection movements, determines left turn treatment and defines ring-barrier structure
  Lane volumes – calculation of lane volumes (HCM 2010 Chapter 31)
  Phase calculation – calculation of the cycle length, green time (splits) allocations, movement capacities, V/C ratios, and Levels of Service (LOS)
  Phasing – calculates phasing data for correct export to Synchro
  Summary sheet – output sheet with calculation results

## Slide 236: QEM Application: Input Sheet 1/2
  Street names – optional
  Intersection lane configuration – required for stand-alone application; not needed for use with NeXTA
  Turning volumes for each movement – required for stand-alone application; not needed for use with NeXTA
  Approach through speeds – important if the speeds are greater than 45 mph; not needed for use with NeXTA
  Presence of pedestrians – should be enabled for urban intersections
  Manual selection of left turn treatment – optional for stand-alone application; not needed for use with NeXTA
  Right Turn on Red (RTOR %) – 50-75% for exclusive right turn lanes, < 10% for shared

## Slide 237: QEM Application: Input Sheet 2/2
  Ideal saturation flow rate (Ideal So) – default value = 1900 vphpl; can be changed to reflect local conditions
  Peak Hour Factor (PHF) – should be entered if known; otherwise, a default value of 0.9 can be used
  Percentage of heavy vehicles (HGV %) – should be entered for local conditions; otherwise, a default value of 3% can be used
  Lost Time (s) per phase – 4 seconds by default; can be changed to reflect local conditions
  Area Type selection – “CBD” (Central business district) and “Other”; should be selected for the analyzed network
  Minimum and maximum desired cycle lengths – by default, the cycle length is between 40 s (minimum) and 150 s (maximum)

## Slide 241: QEM Application: Summary Sheet
  Turning volumes (vph)
  Phase designations
  Number of lanes
  Split durations (s)
  Movement capacities (vph)
  V/C ratios
  Control delays (s)
  Intersection LOS
  Phase data table
Fig. 20 QEM Summary Sheet

## Slide 242: Module 8: VRP Code
https://github.com/xzhou99/Agent-Plus/blob/master/cpp_source_code_v2_VRP/AgentPlus_VRP/AgentPlus/AgentPlus.cpp
Source code link:

## Slide 243
Lagrangian Relaxation Model
Lagarangian Relaxation
Lagarangian Multipliers mean passengers’ profit

## Slide 244
Input Data
Output Data
1. Lagrangian lower bound and primal upper bound
2. Passenger and vehicles’ assignments and time-space routes
Input_node
Input_link
Input_agent
Initial profit of passengers

## Slide 245
Main functions
Generate_string_key():
Including nodeID, passenger ID, and pickup or delivery state
Convenient for visiting in dynamic programming
Such as: n4_1[1]_3[2]_4[2], means node 4 with pickup of p1, delivery of p3 and delivery of p4

## Slide 246
Main Class
Class Name | Major functions | Major variables | Used modules
Node | CalculateCost() | PassengerID, VehicleID, LowerBound, UpperBound | Basic data
VRP_exchange_data //in one node | AddP2VAssignment (int p, int v) | LowerBound, UpperBound, V2PAssignmentVector | Branch & Bound
V2PAssignment //vehicles assigned for each p | AddCompettingVehID (int vehicle_id) | input_prohibited_vehicle_id_vector: not allowable vehicles output_competting_vehicle_id_vector: competing vehicles | Branch & Bound
CVSState //for vehicle scheduling states |  | LabelCost, PrimalLabelCost passenger_service_state | C_time_indexed_state_vector &DP
C_time_indexed_state_vector | update_state (CVSState new_element) | m_VSStateVector //vector of CVSState | DP

## Slide 247
Main variables
For passengers | For vehicles
g_passenger_base_profit[passenger_id] profit of passengers (LR multipliers) | g_time_dependent_state_vector[vehicle_id][t]. m_VSStateVector state vector of a vehicle
competing_vehicle_size competing vehicels | g_ending_state_vector[vehicle_id] final state of a vehicle
input_prohibited_vehicle_id_vector in Branch and Bound, vehicles which cannot serve passenger p | 

## Slide 248
Branch & Bound

## Slide 249
Branch & Bound

## Slide 250
Branch & Bound
Assignment Problem Using Branch-And-Bound Method link:
https://math.stackexchange.com/questions/1466459/assignment-problem-using-branch-and-bound-method

## Slide 251
Dynamic Programming
For vehicle v
For time t
for state w
for outbound of current w’s node i
calculate labelCost of (i,t,w):
if(the state does not exist)
create it
else if(the label cost of the temp state <
label cost of the existing state)
update the cost of the state
Calculate the cost of the node
Update the cost of the node
Loop

## Slide 252
Lagrangian Relaxation for Lower Bound
Sub-gradient algorithm

## Slide 253
Upper bound generates the solution without the profit of passengers.
Lagrangian Relaxation for Lower Bound

## Slide 254
Example
Node | Lower Bound | Upper Bound
0 | 2 | 21
1 (v1-p1) | 10020 (cut) | 
2 (v2-p1) | 10020 (cut) | 
3 (p1 exclusive) | 10020 (cut) | 

## Slide 255: Thank You!
Questions, Comments, and Suggestions are Welcome.
Please Contact:
Xuesong Zhou, Ph.D. Arizona State University
Tempe, AZ 85287
Email: xzhou74@asu.edu